# UMTS ASN1 RUA description

## UTRAN Iuh : Interface RANAP User Adaption

### 25.468 v11.2.0 (2013-03)

Signalling service between the HNB and the HNB-GW

- Transparent transfer of RANAP messages

A   C   D   E   G   I   M   P   R   S   T   U

-- A -- Ansi-41-IDNNS -- C -- Cause CauseMisc CauseProtocol CauseRadioNetwork CauseTransport CN-DomainIndicator Connect ConnectExtensions ConnectIEs ConnectionlessTransfer connectionlessTransfer ConnectionlessTransferExtensions ConnectionlessTransferIEs connectionRequest Context-ID Criticality CriticalityDiagnostics CriticalityDiagnostics-ExtIEs CriticalityDiagnostics-IE-List CriticalityDiagnostics-IE-List-ExtIEs CSGMembershipStatus -- D -- DirectTransfer directTransfer DirectTransferExtensions DirectTransferIEs Disconnect DisconnectExtensions DisconnectIEs disconnectRequest -- E -- ErrorIndication errorIndication ErrorIndicationExtensions ErrorIndicationIEs Establishment-Cause -- G -- Gsm-map-IDNNS -- I -- id-Cause id-CN-DomainIndicator id-Connect id-ConnectionlessTransfer id-Context-ID id-CriticalityDiagnostics id-CSGMembershipStatus id-DirectTransfer id-Disconnect id-ErrorIndication id-Establishment-Cause id-IntraDomainNasNodeSelector id-privateMessage id-RANAP-Message InitiatingMessage IntraDomainNasNodeSelector -- M -- maxNrOfErrors maxPrivateIEs maxProtocolExtensions maxProtocolIEs -- P -- Presence PrivateIE-ID PrivateMessage privateMessage PrivateMessage-IEs ProcedureCode ProtocolIE-ID -- R -- RANAP-Message RoutingParameter RUA-ELEMENTARY-PROCEDURE RUA-ELEMENTARY-PROCEDURES RUA-ELEMENTARY-PROCEDURES-CLASS-1 RUA-ELEMENTARY-PROCEDURES-CLASS-2 RUA-PDU -- S -- SuccessfulOutcome -- T -- TriggeringMessage TypeOfError -- U -- UnsuccessfulOutcome -- ************************************************************** -- -- Elementary Procedure definitions -- -- ************************************************************** RUA-PDU-Descriptions { itu-t (0) identified-organization (4) etsi (0) mobileDomain (0) umts-Access (20) modules (3) rua(5) version1 (1) rUA-PDU-Descriptions (0)} DEFINITIONS AUTOMATIC TAGS ::= BEGIN -- ************************************************************** -- -- IE parameter types from other modules. -- -- ************************************************************** IMPORTS Criticality, ProcedureCode FROM RUA-CommonDataTypes Connect, DirectTransfer, Disconnect, ConnectionlessTransfer, ErrorIndication, PrivateMessage FROM RUA-PDU-Contents id-Connect, id-DirectTransfer, id-Disconnect, id-ConnectionlessTransfer, id-ErrorIndication, id-privateMessage FROM RUA-Constants; -- ************************************************************** -- -- Interface Elementary Procedure Class -- -- ************************************************************** RUA-ELEMENTARY-PROCEDURE ::= CLASS { &InitiatingMessage , &SuccessfulOutcome OPTIONAL, &UnsuccessfulOutcome OPTIONAL, &procedureCode ProcedureCode UNIQUE, &criticality Criticality DEFAULT ignore } WITH SYNTAX { INITIATING MESSAGE &InitiatingMessage [SUCCESSFUL OUTCOME &SuccessfulOutcome] [UNSUCCESSFUL OUTCOME &UnsuccessfulOutcome] PROCEDURE CODE &procedureCode [CRITICALITY &criticality] } -- ************************************************************** -- -- Interface PDU definitions -- -- ************************************************************** RUA-PDU ::= CHOICE { initiatingMessage InitiatingMessage, successfulOutcome SuccessfulOutcome, unsuccessfulOutcome UnsuccessfulOutcome, ... } InitiatingMessage ::= SEQUENCE { procedureCode RUA-ELEMENTARY-PROCEDURE.&procedureCode ({RUA-ELEMENTARY-PROCEDURES}), criticality RUA-ELEMENTARY-PROCEDURE.&criticality ({RUA-ELEMENTARY-PROCEDURES}{@procedureCode}), value RUA-ELEMENTARY-PROCEDURE.&InitiatingMessage ({RUA-ELEMENTARY-PROCEDURES}{@procedureCode}) } SuccessfulOutcome ::= SEQUENCE { procedureCode RUA-ELEMENTARY-PROCEDURE.&procedureCode ({RUA-ELEMENTARY-PROCEDURES}), criticality RUA-ELEMENTARY-PROCEDURE.&criticality ({RUA-ELEMENTARY-PROCEDURES}{@procedureCode}), value RUA-ELEMENTARY-PROCEDURE.&SuccessfulOutcome ({RUA-ELEMENTARY-PROCEDURES}{@procedureCode}) } UnsuccessfulOutcome ::= SEQUENCE { procedureCode RUA-ELEMENTARY-PROCEDURE.&procedureCode ({RUA-ELEMENTARY-PROCEDURES}), criticality RUA-ELEMENTARY-PROCEDURE.&criticality ({RUA-ELEMENTARY-PROCEDURES}{@procedureCode}), value RUA-ELEMENTARY-PROCEDURE.&UnsuccessfulOutcome ({RUA-ELEMENTARY-PROCEDURES}{@procedureCode}) } -- ************************************************************** -- -- Interface Elementary Procedure List -- -- ************************************************************** RUA-ELEMENTARY-PROCEDURES RUA-ELEMENTARY-PROCEDURE ::= { RUA-ELEMENTARY-PROCEDURES-CLASS-1 | RUA-ELEMENTARY-PROCEDURES-CLASS-2 , ... } RUA-ELEMENTARY-PROCEDURES-CLASS-1 RUA-ELEMENTARY-PROCEDURE ::= { ... } RUA-ELEMENTARY-PROCEDURES-CLASS-2 RUA-ELEMENTARY-PROCEDURE ::= { connectionRequest | directTransfer | disconnectRequest | connectionlessTransfer | errorIndication | privateMessage, ... } -- ************************************************************** -- -- Interface Elementary Procedures -- -- ************************************************************** connectionRequest RUA-ELEMENTARY-PROCEDURE ::= { INITIATING MESSAGE Connect PROCEDURE CODE id-Connect CRITICALITY ignore } directTransfer RUA-ELEMENTARY-PROCEDURE ::= { INITIATING MESSAGE DirectTransfer PROCEDURE CODE id-DirectTransfer CRITICALITY ignore } disconnectRequest RUA-ELEMENTARY-PROCEDURE ::= { INITIATING MESSAGE Disconnect PROCEDURE CODE id-Disconnect CRITICALITY ignore } connectionlessTransfer RUA-ELEMENTARY-PROCEDURE ::= { INITIATING MESSAGE ConnectionlessTransfer PROCEDURE CODE id-ConnectionlessTransfer CRITICALITY ignore } errorIndication RUA-ELEMENTARY-PROCEDURE ::= { INITIATING MESSAGE ErrorIndication PROCEDURE CODE id-ErrorIndication CRITICALITY ignore } privateMessage RUA-ELEMENTARY-PROCEDURE ::= { INITIATING MESSAGE PrivateMessage PROCEDURE CODE id-privateMessage CRITICALITY ignore } END -- ************************************************************** -- -- PDU definitions for RUA. -- -- ************************************************************** RUA-PDU-Contents { itu-t (0) identified-organization (4) etsi (0) mobileDomain (0) umts-Access (20) modules (3) rua(5) version1 (1) rUA-PDU-Contents (1) } DEFINITIONS AUTOMATIC TAGS ::= BEGIN -- ************************************************************** -- -- IE parameter types from other modules. -- -- ************************************************************** IMPORTS Cause, CriticalityDiagnostics, Context-ID, CN-DomainIndicator, CSGMembershipStatus, IntraDomainNasNodeSelector, RANAP-Message, Establishment-Cause FROM RUA-IEs ProtocolExtensionContainer{}, ProtocolIE-ContainerList{}, ProtocolIE-Container{}, ProtocolIE-Single-Container{}, PrivateIE-Container{}, RUA-PRIVATE-IES, RUA-PROTOCOL-EXTENSION, RUA-PROTOCOL-IES FROM RUA-Containers id-Cause, id-CriticalityDiagnostics, id-Context-ID, id-CN-DomainIndicator, id-CSGMembershipStatus, id-RANAP-Message, id-IntraDomainNasNodeSelector, id-Establishment-Cause FROM RUA-Constants; -- ************************************************************** -- -- Connect -- -- ************************************************************** Connect ::= SEQUENCE { protocolIEs ProtocolIE-Container { {ConnectIEs} }, protocolExtensions ProtocolExtensionContainer { {ConnectExtensions} } OPTIONAL, ... } ConnectIEs RUA-PROTOCOL-IES ::= { { ID id-CN-DomainIndicator CRITICALITY reject TYPE CN-DomainIndicator PRESENCE mandatory } | { ID id-Context-ID CRITICALITY reject TYPE Context-ID PRESENCE mandatory } | { ID id-IntraDomainNasNodeSelector CRITICALITY ignore TYPE IntraDomainNasNodeSelector PRESENCE optional } | { ID id-Establishment-Cause CRITICALITY reject TYPE Establishment-Cause PRESENCE mandatory } | { ID id-RANAP-Message CRITICALITY reject TYPE RANAP-Message PRESENCE mandatory }, ... } ConnectExtensions RUA-PROTOCOL-EXTENSION ::= { { ID id-CSGMembershipStatus CRITICALITY ignore EXTENSION CSGMembershipStatus PRESENCE optional }, ... } -- ************************************************************** -- -- Direct Transfer -- -- ************************************************************** DirectTransfer ::= SEQUENCE { protocolIEs ProtocolIE-Container { {DirectTransferIEs} }, protocolExtensions ProtocolExtensionContainer { {DirectTransferExtensions} } OPTIONAL, ... } DirectTransferIEs RUA-PROTOCOL-IES ::= { { ID id-CN-DomainIndicator CRITICALITY reject TYPE CN-DomainIndicator PRESENCE mandatory } | { ID id-Context-ID CRITICALITY reject TYPE Context-ID PRESENCE mandatory } | { ID id-RANAP-Message CRITICALITY reject TYPE RANAP-Message PRESENCE mandatory }, ... } DirectTransferExtensions RUA-PROTOCOL-EXTENSION ::= { ... } -- ************************************************************** -- -- Disconnect -- -- ************************************************************** Disconnect ::= SEQUENCE { protocolIEs ProtocolIE-Container { {DisconnectIEs} }, protocolExtensions ProtocolExtensionContainer { {DisconnectExtensions} } OPTIONAL, ... } DisconnectIEs RUA-PROTOCOL-IES ::= { { ID id-CN-DomainIndicator CRITICALITY reject TYPE CN-DomainIndicator PRESENCE mandatory } | { ID id-Context-ID CRITICALITY reject TYPE Context-ID PRESENCE mandatory } | { ID id-Cause CRITICALITY reject TYPE Cause PRESENCE mandatory } | { ID id-RANAP-Message CRITICALITY reject TYPE RANAP-Message PRESENCE conditional }, -- RANAP message shall be included if Cause value is "normal" ... } DisconnectExtensions RUA-PROTOCOL-EXTENSION ::= { ... } -- ************************************************************** -- -- Connectionless Transfer -- -- ************************************************************** ConnectionlessTransfer ::= SEQUENCE { protocolIEs ProtocolIE-Container { {ConnectionlessTransferIEs} }, protocolExtensions ProtocolExtensionContainer { {ConnectionlessTransferExtensions} } OPTIONAL, ... } ConnectionlessTransferIEs RUA-PROTOCOL-IES ::= { { ID id-RANAP-Message CRITICALITY reject TYPE RANAP-Message PRESENCE mandatory }, ... } ConnectionlessTransferExtensions RUA-PROTOCOL-EXTENSION ::= { ... } -- ************************************************************** -- -- ERROR INDICATION -- -- ************************************************************** ErrorIndication ::= SEQUENCE { protocolIEs ProtocolIE-Container { {ErrorIndicationIEs} }, protocolExtensions ProtocolExtensionContainer { {ErrorIndicationExtensions} } OPTIONAL, ... } ErrorIndicationIEs RUA-PROTOCOL-IES ::= { { ID id-Cause CRITICALITY ignore TYPE Cause PRESENCE mandatory } | { ID id-CriticalityDiagnostics CRITICALITY ignore TYPE CriticalityDiagnostics PRESENCE optional }, ... } ErrorIndicationExtensions RUA-PROTOCOL-EXTENSION ::= { ... } -- ************************************************************** -- -- PRIVATE MESSAGE -- -- ************************************************************** PrivateMessage ::= SEQUENCE { privateIEs PrivateIE-Container {{PrivateMessage-IEs}}, ... } PrivateMessage-IEs RUA-PRIVATE-IES ::= { ... } END -- ************************************************************** -- -- Information Element Definitions -- -- ************************************************************** RUA-IEs { itu-t (0) identified-organization (4) etsi (0) mobileDomain (0) umts-Access (20) modules (3) rua(5) version1 (1) rUA-IEs (2) } DEFINITIONS AUTOMATIC TAGS ::= BEGIN IMPORTS maxNrOfErrors FROM RUA-Constants Criticality, ProcedureCode, ProtocolIE-ID, TriggeringMessage FROM RUA-CommonDataTypes ProtocolExtensionContainer{}, RUA-PROTOCOL-EXTENSION FROM RUA-Containers; CN-DomainIndicator ::= ENUMERATED { cs-domain, ps-domain } CSGMembershipStatus ::= ENUMERATED { member, non-member, ... } Establishment-Cause ::= ENUMERATED { emergency-call, normal-call, ... } Context-ID ::= BIT STRING (SIZE(24)) IntraDomainNasNodeSelector ::= SEQUENCE { version CHOICE { release99 SEQUENCE { cn-Type CHOICE { gsm-Map-IDNNS Gsm-map-IDNNS, ansi-41-IDNNS Ansi-41-IDNNS } }, later SEQUENCE { futurecoding BIT STRING (SIZE (15)) } } } Gsm-map-IDNNS ::= SEQUENCE { routingbasis CHOICE { localPTMSI SEQUENCE { routingparameter RoutingParameter }, tMSIofsamePLMN SEQUENCE { routingparameter RoutingParameter }, tMSIofdifferentPLMN SEQUENCE { routingparameter RoutingParameter }, iMSIresponsetopaging SEQUENCE { routingparameter RoutingParameter }, iMSIcauseUEinitiatedEvent SEQUENCE { routingparameter RoutingParameter }, iMEI SEQUENCE { routingparameter RoutingParameter }, spare2 SEQUENCE { routingparameter RoutingParameter }, spare1 SEQUENCE { routingparameter RoutingParameter } }, -- dummy is not used in this version of the specification and -- it should be ignored by the receiver. dummy BOOLEAN } Ansi-41-IDNNS ::= BIT STRING (SIZE (14)) RANAP-Message ::= OCTET STRING RoutingParameter ::= BIT STRING (SIZE (10)) -- ************************************************************** -- -- Cause IE -- -- ************************************************************** Cause ::= CHOICE { radioNetwork CauseRadioNetwork, transport CauseTransport, protocol CauseProtocol, misc CauseMisc, ... } CauseRadioNetwork ::= ENUMERATED { normal, connect-failed, network-release, unspecified, ... } CauseTransport ::= ENUMERATED { transport-resource-unavailable, unspecified, ... } CauseProtocol ::= ENUMERATED { transfer-syntax-error, abstract-syntax-error-reject, abstract-syntax-error-ignore-and-notify, message-not-compatible-with-receiver-state, semantic-error, unspecified, abstract-syntax-error-falsely-constructed-message, ... } CauseMisc ::= ENUMERATED { processing-overload, hardware-failure, o-and-m-intervention, unspecified, ... } -- ************************************************************** -- -- CriticalityDiagnostics -- -- ************************************************************** CriticalityDiagnostics ::= SEQUENCE { procedureCode ProcedureCode OPTIONAL, triggeringMessage TriggeringMessage OPTIONAL, procedureCriticality Criticality OPTIONAL, iEsCriticalityDiagnostics CriticalityDiagnostics-IE-List OPTIONAL, iE-Extensions ProtocolExtensionContainer { {CriticalityDiagnostics-ExtIEs} } OPTIONAL, ... } CriticalityDiagnostics-IE-List ::= SEQUENCE (SIZE (1..maxNrOfErrors)) OF SEQUENCE { iECriticality Criticality, iE-ID ProtocolIE-ID, typeOfError TypeOfError, iE-Extensions ProtocolExtensionContainer { {CriticalityDiagnostics-IE-List-ExtIEs} } OPTIONAL, ... } CriticalityDiagnostics-IE-List-ExtIEs RUA-PROTOCOL-EXTENSION ::= { ... } CriticalityDiagnostics-ExtIEs RUA-PROTOCOL-EXTENSION ::= { ... } TypeOfError ::= ENUMERATED { not-understood, missing, ... } END -- ************************************************************** -- -- Common definitions -- -- ************************************************************** RUA-CommonDataTypes { itu-t (0) identified-organization (4) etsi (0) mobileDomain (0) umts-Access (20) modules (3) rua(5) version1 (1) rUA-CommonDataTypes (3) } DEFINITIONS AUTOMATIC TAGS ::= BEGIN -- ************************************************************** -- -- Extension constants -- -- ************************************************************** maxPrivateIEs INTEGER ::= 65535 maxProtocolExtensions INTEGER ::= 65535 maxProtocolIEs INTEGER ::= 65535 -- ************************************************************** -- -- Common Data Types -- -- ************************************************************** Criticality ::= ENUMERATED { reject, ignore, notify } Presence ::= ENUMERATED { optional, conditional, mandatory } ProcedureCode ::= INTEGER (0..255) PrivateIE-ID ::= CHOICE { local INTEGER (0..65535), global OBJECT IDENTIFIER } ProtocolIE-ID ::= INTEGER (0..maxProtocolIEs) TriggeringMessage ::= ENUMERATED { initiating-message, successful-outcome, unsuccessful-outcome } END -- ************************************************************** -- -- Constant definitions -- -- ************************************************************** RUA-Constants { itu-t (0) identified-organization (4) etsi (0) mobileDomain (0) umts-Access (20) modules (3) rua(5) version1 (1) rUA-Constants (4) } DEFINITIONS AUTOMATIC TAGS ::= BEGIN IMPORTS ProcedureCode, ProtocolIE-ID FROM RUA-CommonDataTypes; -- ************************************************************** -- -- Elementary Procedures -- id-Connect ProcedureCode ::= 1 id-DirectTransfer ProcedureCode ::= 2 id-Disconnect ProcedureCode ::= 3 id-ConnectionlessTransfer ProcedureCode ::= 4 id-ErrorIndication ProcedureCode ::= 5 id-privateMessage ProcedureCode ::= 6 -- ************************************************************** -- -- Lists -- -- ************************************************************** maxNrOfErrors INTEGER ::= 256 -- ************************************************************** -- -- IEs -- -- ************************************************************** id-Cause ProtocolIE-ID ::= 1 id-CriticalityDiagnostics ProtocolIE-ID ::= 2 id-Context-ID ProtocolIE-ID ::= 3 id-RANAP-Message ProtocolIE-ID ::= 4 id-IntraDomainNasNodeSelector ProtocolIE-ID ::= 5 id-Establishment-Cause ProtocolIE-ID ::= 6 id-CN-DomainIndicator ProtocolIE-ID ::= 7 id-CSGMembershipStatus ProtocolIE-ID ::= 9 END